## Slide 1: Hughes Airwest DC-9 vs. USMC F-4B

## Slide 2: June 6th, 1971
McDonnell Douglas DC-9-31
USMC Douglas F-4B Phantom II
50 killed, 1 survivor
Duarte, California

## Slide 3: DC-9-31
Twin-engine, single-aisle jet airliner.
Designed for frequent, short flights.
-Artist impression of N9345

## Slide 4: F-4B Phantom II
Two seat, twin-engine, all-weather, long-range supersonic jet interceptor fighter/ fighter-bomber
Originally developed for U.S. Navy by McDonnell Aircraft, later adopted by the U.S.M.C and U.S.A.F.
-U.S. Marine Corps F-4B Phantom II similar to the one involved

## Slide 5: DC-9 Flight 709 History
Put into service in 1969
Scheduled route between L.A., CA and Seattle, WA.
5 stopovers
5,542 airframe hours
Pilot: Cpt. Nicolay
Co-Pilot: 1st Officer Bruner

## Slide 6: F-4B ‘458’ Flight History
Active since April 15, 1964
Consigned to the U.S. Marine Corps
Two plane cross-country flight
Pilot: Lt. Phillips
RIO: Lt. Schiess

## Slide 7: Issues with the 458
Inoperative radio
Inoperative transponder
Oxygen system leak
Degraded radar system

## Slide 8: What happened?
Worsening weather conditions
‘458’ elevation: 1,000 ft.  15,500 ft.
Aileron roll: 360°
Radar failed
2 points of impact
10 Feet

## Slide 10: Collision

## Slide 11
-Crash site of Flight 706 in the San Gabriel Mountains

## Slide 12
-Impact site of ‘458’ on Mount Bliss , approximately 1 mile from the airline wreckage

## Slide 13: Survival
Impossible for commercial passengers
  Collision
  Disintegration
  Crash
  Fire
Both crewmembers of Phantom could have lived
  Design flaw in ejector seat

## Slide 14: Probable Cause
Failure to see each other
High closure rate
IFR/ VFR
Failing equipment

## Slide 15: Recommendations
Video/audio surveillance in ATC facilities
Air traffic controlled airspace for entire duration of all IFR air traffic
Improved definitive procedures for spotting/tracking of code 7700 aircraft

## Slide 16: Additional Recommendations
FAA & DOD cooperate to develop program to mitigate collisions and near-misses between civilian and military aircraft
DOD restrict high-speed, low-altitude aircraft operation in civilian air corridors, consider collision avoidance technologies on military aircraft, and make military pilots aware of FAA’s radar advisory service

## Slide 17: References
National Transportation Safety Board. (30 August 1972). Aircraft accident report: Hughes Air West DC-9, N9345 and U.S. Marine Corps F-4B, 151458, near Duarte, California, June 6, 1971, p. 1-50. [PDF] [Last Accessed 08 October 2012].
Federal Aviation Administration. (26 July 2012). Air Traffic Control Section 2. Beacon Systems. [ONLINE] Available at: http://www.faa.gov/. [Last Accessed 08 October 2012].
Aviation Safety Network. (24 October 2011). ASN Aircraft accident McDonnell Douglas DC-9-31 N9345 Duarte, CA. [ONLINE] Available at: aviation-safety.net/. [Last Accessed 08 October 2012].
SmugMug, Inc. (2012). June 6, 1971, Hughes Air West / USMC, McDonnell Douglas DC-9 (N9345) / McDonnell Douglas F-4B (151458) Mid-Air Collision near Duarte, CA- LOSTFLIGHTS Historical Aviation Studies and Research. [ONLINE] Available at: http://lostflights.smugmug.com/. [Last Accessed 08 October 2012].
The Portsmouth Times, AP. (19 June 1971). Military Craft Due to Fly by Civilian Rules, p. 7. [PDF] [Last Accessed 08 October 2012].
The Deseret News. (17 June 1971). 10 More Feet-50 Lives, p. 1. [PDF] [Last Accessed 08 October 2012].